## Slide 1: P4:Programming Protocol-independent Packet Processors
Presented By: Subhrendu Chattopadhyay
Systems and Mobile Research Lab, IIT Kharagpur
Notes: Today I’ll be talking about one of recent trends in network architecture i.e. P4 which is formally known as Programming Protocol-independent Packet Processors. But before jumping into the actual topic let me take latitude with the back story.
Recently we were attending Hotnets 2020 and some of the papers were talking about P4 paradigm and data plane. For some of us it was difficult to understand those papers. Therefore, Abhijit asked me whether I can give a short presentation on P4 during our weekly research discussion as I have started exploring this domain.

## Slide 2: Outline
Evolution of Programmable network
PISA: Protocol independent Switch Architecture
P4: Workflow
P4: Examples
P4: Recent Papers (May be in the next meeting)
Notes: I have tried to keep this talk free from any pre-requisites apart from basic networking related terms. So, please feel free to stop me at anytime if you need any clarification.
Now, the brief outline of the talk is as follows. I’ll start with the programmable network and it’s evolution, since P4 is one of the component of programmable network design. This discussion will lead us to the PISA architecture. From PISA we will see why P4 is necessary followed by the components, workflow and an example program. Finally, I have incorporated a few of the recent papers which will help us to to the understand what are being done in this area.

## Slide 3: Network 101
Given a connected network
Find path from source to destination
H1
H2
Notes: As promised, let’s start with Network 101. Consider there are two hosts; H1 and H2. They are connected via 3 different switches. Now the basic objective of network is to send a packet from one device to another. In this case from H1 to H2.

## Slide 4: Switch and Control/Data plane
Switch Architecture
Data Plane
Control Plane
Interfaces
Packets
Management Plane
Configurable Parameters
Notes: Now, how does a switch work? So, basically a switch has multiple input and output interfaces. Once a packet arrives at an input interface, the task of switch is to identify the output interface. Additionally the switch may add, remove and/or modify some of the header fields of the packet. So, essentially the switch can be abstracted as a function which transforms the packet. This switch functionality depends on three 3 different sub-modules or planes which forms the switch architecture.
Management Plane: When we buy a switch it needs to be configured before plugging it into the network, right? For example, we need to fill up IP, Subnet mask, Gateway, DHCP, DNS etc. This is done inside the management plane. The management plane is responsible for managing of configuration parameters and monitoring of network equipment.
Control Plane: Once the configuration parameters are updated, there are some algorithms which decides behavior of the packet forwarding. For example, these algorithm collects the network topology, calculates the input output port mapping based on the topology and management plane information. Additionally based on the applied algorithm (popularly known as protocols) the packet headers are modified.
Data plane: The results of the control plane generates forwarding/routing tables. The task of data plane is to see the table and apply the actual transformation on the packets.

## Slide 5: Traditional Switch Architecture
Configurable (by Sys. Admins)
Rarely programmable (Firmware update)
Protocol specific tasks
Vendor specific functionalities
Data Plane
Control Plane
Control plane CPU
Switch ASIC
Lookup Table (Policy)
Table Management
Config Table
Notes: The traditional switch architecture is composed of two distinct part. Control plane and Data plane. There are tables inside a switch control plane which store the management configurations. Based on these configurations the protocol related algorithms are run inside the control plane CPU. The outputs are stored inside a lookup table at data plane. Whenever a packet comes to the interface, the data plane ASIC (Application specific switch Integrated Circuit) searches the lookup table and sends it to the output interface after performing the packet transformation.
This switch architecture is very old and has some problem. These switches can be configured by network administrators and rarely support programmability by providing firmware updates. Additionally, these devices supports fixed functionalities based on the supported protocols. Which means, if you want transparent VPN in your home wifi-router and you have bought a TPlinkWR-740N like me, then you can not do it unless you update the device with a custom firmware.
Although there are RFCs and IEEE standards for protocols, different vendors implement protocols differently. In-fact Sandip sir told me once, that this is the reason large scale network administrators prefer to buy the equipment from same manufacturer.

## Slide 6: Programmable Network
Traditional Switch Internals
  Switch OS running variants of Linux/Unix
  Device specific drivers
  User space protocol implementation
Basic question
  Why it requires so long to add a feature to the network equipments?
Example
  VxLAN  Defined in 2010  Deployed in 2014
  What happened during these 4 years?
Notes: If we look under the the hood of a network equipment most of the time we find a switch OS, which is a variant of Linux or Unix. We also find device specific device drivers based on the used chips. The protocols running inside the switches are written as user space implementation or as loadable kernel modules.
Even though most of the equipment has similar constructions, the basic question is why does it need so long to add a new protocol to the devices?
For example, lets see the VxLAN case. The RFC for VxLAN came in 2010 but the first commercially available device were out in 2014. So, it took 4 years to deploy the protocol. What happened during these years?

## Slide 7: Programmable Network
Life cycle
By the time the feature is available
  No longer solve the problem
  Expensive: Need hardware change
  We have already found a way around 😝
Courtesy: N. McKewon https://www.youtube.com/watch?v=zR88Nlg3n3g
Enterprise
Network Equip. Vendor
Software Team
ASIC Team
I need this feature
Check RFC/ IETF drafts
Feature set
Few weeks
Tables
Few years!!!
Notes: To answer this question, we need to look into the manufacturing life-cycle of the network equipment which was described by Nick McKeown in his lecture at BareFoot Technology. The customers or enterprises requested the VxLAN feature to the network equipment vendors like CISCO. The vendor then consulted the RFCs and IETF drafts to understand the exact functionalities. Then they consulted their software team. The software team replied, “Yes, we can do it in few weeks”. Then they asked their ASIC team. The ASIC team estimated 2.5-3 years. And this was not a big change. Only some tables needs to be added or altered. After this the entire things were tested. So, the final deployment of VxLAN took 4 years.
Now, If the new protocol deployment takes took that much time, when the feature is available it no longer solves the problem as the problem has been changed over the years. Also, the customer now needs to change the hardware which increases the capital expenditure. And more importantly, by the time the feature is available, people have already found another way around.
So, the bottleneck were the ASIC team. And that’s because the hardware engineers were given the responsibility of network design and that's a bad idea.
Therefore, the research community felt that, to tackle this rigidness the network needs to be programmable where new protocol implementation does not have to depend on the hardware engineers. Instead software changes will be sufficient for rapid deployment of new features.

## Slide 8: Software Defined Networking (SDN)
Software Defined Networking (SDN)
  Program network
  Rapid deployment
  Software centric
Data Plane
Dumb Control Plane
Policies/Signaling via OpenFlow API
Controller
Data Plane
Dumb Control Plane
Match | Action
ETH_DST=A1 | Drop
ETH_DST=A2 & ETH_TYPE=B2 | Port 2
IPV4_SRC=P1 & IPV4_DST=P2 | Push VLAN header
Notes: This was the core motivation behind software defined networking popularly know as SDN. SDN separates the control plane from the network equipments and introduces a separate control plane. Each entity in the control plane are called controllers. The devices were left with a dumb control plane which does not take decisions. Instead it forwards queries raised by data plane to the controllers via standard API. OpenFlow is one of the popular implementation of such API. In SDN if you want to change the protocol behavior, you write a controller application and execute it in the controller. That’s it.
In the data plane we still have a table known as flow tables. This consists of a match field and corresponding action field. There are other columns also which I have omitted for the sake of simplicity. This table is filled-up by the control plane. The data plane only looks-up and take appropriate actions on the packets if the match is found.

## Slide 9: Why P4?
SDN provides
  Rapid prototyping of control plane
  OpenFlow is header field/protocol dependent
  Slow release cycle
Why OpenFlow is not enough?
  Custom Header fields
  Data plane evolution
  In-band/ In-network processing
Chart: OpenFlow Match Fields
| 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5
Supported Fields | 12 | 15 | 36 | 40 | 41 | 44
Notes: Although SDN enables rapid prototyping, it is still dependent on the set of protocol supported. For example, different versions of the OpenFlow supports different set of match fields as shown in the plot. Now if you want to develop a new protocol which isn’t supported by OpenFlow, you have to wait till the new release or you need to write your own API which is cumbersome.
So OpenFlow is not sufficient due to the following reasons.
OpenFlow is protocol dependent. Therefore, adding custom header takes significant effort. Now if you want to do a data plane optimization by removing header you need to again modify the OpenFlow sources. Additionally, if someone wishes to introduce a new type of packet processing action, OpenFlow is not the correct tool.
So the bottom line is, SDN provides control plane programmability; But we need something more. Therefore, the solution lies in a different type of switch architecture.

## Slide 10: Programmable data plane
Programmable Data Plane
Dumb Control Plane
Data plane Prog.
Policies/Signaling
Controller
Upload Program
PISA
  Protocol Independent Switch Architecture
  Language ?
Notes: This new architecture enables programmability in the data plane and called as PISA or Protocol Independent Switch Architecture. It converts the data plane into a piece of software.

## Slide 11: PISA Pipelines: Under the bonnet
Parser
De-Parser
Programmer declares the headers that should be recognized and their order in the packet
Programmer defines the tables and the exact processing algorithm
Programmer declares how the output packet will look on the wire
Mem
ALU
Pkt. with multiple header arrives
Match+Action
Notes: PISA enables pipeline processing. A PISA switch has a programmable parser, a few programmable [match + action] tables called as pipeline elements, and a programmable de-parser. The programmable parser and de-parser enables addition, removal and customization of packet headers. The programmable pipeline elements introduces addition, removal and alteration of actions.
Lets see how the PISA switch works. <C> Lets say a packet comes to one of the interfaces of the switch. The colored boxes are different header fields followed by payload. <C> The parser can sperate the headers and send them to the pipeline element. Now each pipeline element transforms the header fields <C> <C> <C>. Finally, the de-parser <C> reassembles the header and the payload <C> and sends it to the outgoing interface queue.

## Slide 12: Compiler for PISA
System | Compiler | Target Device
Computer | JAVA/Python/Go etc. | CPU
Graphics | OpenCL | GPU
Signal Processing | MATLAB | DSP
Machine Learning | TensorFlow | TPU
Network (PISA) | ??? | ASIC/FPGA
We need a compiler/language to work with PISA
Notes: With the new PISA switches in our hand, we now need to look at, how to use it. One option is we can modify the OpenFlow to make it workable with the PISA. But that’s complex and increases programmer overhead. So, lets see how the other systems have reduced the programmer overhead.
In computer, we write high level programs and rely on the domain specific compilers to reduce the overhead. Similarly, OpenCL provides compiler level abstraction for GPU, MATLAB for DSP, TensorFlow for TPU.
So, the answer is, Forget event driven programming used in traditional switches. Forget C/C++/Assembly level programming. Let’s move to a high level programming language and domain specific compiler. So, we need a language/ compiler which provides target independence for ASIC or FPGA pipeline chips used in PISA.

## Slide 13: P4: Programming Protocol-independent Packet Processors
High level language for data plane program
Objectives
  Header field independence
  Protocol independence
  Target/Device independence
Notes: Here comes the main topic of the talk after this long prelude and build-up.
So, P4 provides a target independent compiler and high level language for PISA switches. It was resulted from the 3 objectives. Header Independence, Protocol Independence, Device Independence

## Slide 14: P4: Workflow
P4 Program
PISA
Switch
P4 Device Architecture
P4 Compiler
Target Specific Binary
Vendor Supplied
User Defined
Notes: Now in the P4 world, the vendor not only supplies the device. It also supplies the Device Architecture related library files and a target specific compiler. Using the last two artifacts an user can write his/her own P4 program which generates the device specific binary.

## Slide 15: P4: Example (V1 model)
https://github.com/opendaylight/p4plugin/blob/master/apps/simple-router/src/main/resources/p4/simple-router.p4
/* SWITCH */
V1Switch(
MyParser(),
MyVerifyChecksum(),
MyIngress(),
MyEgress(),
MyComputeChecksum(),
MyDeparser()
) main;
#include <core.p4>
#include <v1model.p4>
/* HEADERS */
header ethernet_t { ... }
header ipv4_t { ... }
struct metadata { ... }
struct headers {
ethernet_t ethernet;
ipv4_t ipv4;
}
/* PARSER */
parser MyParser(packet_in packet,
out headers hdr,
inout metadata meta,
inout standard_metadata_t standard_metadata) { ... }
/* CHECKSUM VERIFICATION */
control MyVerifyChecksum(inout headers hdr, inout metadata meta) { ... }
/* INGRESS PROCESSING */
control MyIngress(inout headers hdr,
inout metadata meta,
inout standard_metadata_t standard_metadata) { ... }
/* EGRESS PROCESSING */
control MyEgress(inout headers hdr,
inout metadata meta,
inout standard_metadata_t standard_metadata) { ... }
/* CHECKSUM COMPUTATION */
control MyComputeChecksum(inout headers hdr, inout metadata meta) { ... }
/* DEPARSER */
control MyDeparser(packet_out packet, in headers hdr) { ... }
Block-9
Entry Point
Block-1
Block-2
Block-3
Block-8
Block-4
Block-5
Block-6
Block-7
Notes: For example, One of the popular Switch architecture is V1 model. Say I have a PISA switch which supports V1 model, then I can write the following P4 program. The code can be found in P4 repository.
If the look at the structure of the program, block-1 provides the standard library and the model specific library. In block-2 we can define our custom headers. Block-3 and Block-8 provides the programmable parser and de-parser respectively. Block-4 and 7 provides checksum verification and checksum computation. Block-5 and 6 provides the ingress processing and egress processing.
Finally, the order of pipeline execution is decided in block-9 which the entry point main method.

## Slide 16: P4: Example (V1 model)
Define Header fields
Custom | Standard | Standard | All Headers
header mTag_t { bit<8> up1; bit<8> up2; bit<8> down1; bit<8> down2; bit<16> ethertype; } | header ethernet_t { bit<48> dst_addr; bit<48> src_addr; bit<16> eth_type; } | header ipv4_t { bit<4> version; bit<8> diffserv; ... bit<32> srcAddr; bit<32> dstAddr; } | struct headers{ ethernet_t ethernet; ipv4_t ipv4; mTag_t mTag; }
Notes: As mentioned, P4 provides the custom header. For this we only need to specify the bit position and the field name along with the customized protocol name. In this example, the ethernet_t and ipv4_t are standard protocol headers. Whereas, the mTag_t given in the extreme left is an example of custom header addition.

## Slide 17: P4: Example (V1 model)
Define Parser
parser MyParser(packet_in packet, out headers hdr, inout metadata meta){ state start { transition parse_ethernet; } . . . | state parse_ethernet { packet.extract(hdr.ethernet); transition select(hdr.ethernet.etherType) { TYPE_IPV4: parse_ipv4; default: accept; } } state parse_ipv4 { packet.extract(hdr.ipv4); transition accept; } }
Notes: Once the headers are defined, we need to program the parser. My example parser is invoked when a “packet_in” event occurs and generates a parsed header and corresponding meta data. For simplicity I have not shown the mTag parsing here which can be done similarly.

## Slide 18: P4: Example (V1 model)
Define Parser
  State machine
  Invoke “packet_in packet”
  Output “headers hdr”
  Input/Output “metadata meta”
start
parse_ethernet
accept
parse_ipv4
accept
reject
Notes: The parser also generates a state machine to identify valid field entries.

## Slide 19: P4: Example (V1 model)
Define Control Blocks
  Executed in Match-Action Pipeline elements
control MyVerifyChecksum(inout headers hdr, inout metadata meta) { . . . } control MyIngress(inout headers hdr, inout metadata meta) {. . .} | control MyEgress(inout headers hdr, inout metadata meta) { . . . } control MyComputeChecksum(inout headers hdr, inout metadata meta) { . . . }
control MyDeparser(packet_out packet, in headers hdr) { . . . } | 
Parser
De-Parser
Notes: If you remember the PISA animation, once the packets are parsed the headers are sent to the match-action pipeline elements. In our case, we have 4 pipeline elements. 1rst for checking the checksum of the incoming packet followed by ingress and egress processing. Finally before sending to the de-parser checksum of the transformed packet is recomputed.

## Slide 20: P4: Example (V1 model)
Define Control Blocks
  PISA: Match-Action-Decide
  P4: Table- Action-Apply
control MyIngress(inout headers hdr, inout metadata meta){ action drop() { . . . } action ipv4_forward(macAddr_t dstAddr, egressSpec_t port) { . . . } table ipv4_lpm { . . . } apply { . . . } }
Mem
ALU
Table
Action
}
Apply
Notes: In P4 each match-action pipeline elements are called as control block. Each control block has 3 parts. Tables, Actions and Apply. We’ll discuss them one by one.

## Slide 21: P4: Example (V1 model)
Define Control Blocks
  Define Actions
action drop() { mark_to_drop(); } action ipv4_forward(macAddr_t dstAddr, egressSpec_t port) { standard_metadata.egress_spec = port; hdr.ethernet.srcAddr = hdr.ethernet.dstAddr; hdr.ethernet.dstAddr = dstAddr; //Nxt hop hdr.ipv4.ttl = hdr.ipv4.ttl - 1; }
Mem
ALU
Notes: This sample block defines two actions. Drop and ipv4_forwarding. Notice that, here for ipv4_forwarding we need a forwarding table containing match field and egress port.

## Slide 22: P4: Example (V1 model)
Define Control Blocks
  Define Tables
table ipv4_lpm { key = { hdr.ipv4.dstAddr: exact; } actions = { ipv4_forward; drop; NoAction; // Library Defined } size = 1024; // Limit of table default_action = NoAction(); }
Mem
ALU
action drop() . . . action ipv4_forward() . . .
Notes: This snippet describes the table. Here key is the ipv4.destAddr. The permitted actions can be one of previously defined actions.

## Slide 23: P4: Example (V1 model)
table ipv4_lpm { key = { hdr.ipv4.dstAddr: exact; } actions = { ipv4_forward; drop; NoAction; // Library Defined } size = 1024; // Limit of table default_action = NoAction(); }
action drop() . . . action ipv4_forward(dstAddr, port) . . .
Key | Action | Action Data
192.168.0.1 | ipv4_forward | 11:22:33:44:55:66, 2
202.1.0.1 | Drop | -------------------------
192.168.2.1 | Ipv4_forward | AA:BB:CC:DD:EE:FF, 1
Default Action | Default Action Data
NoAction () | None
Dumb Control Plane
Notes: Once the P4 code executes, the control plane inserts the table entries as shown above. Since, the forwarding action also requires additional data like destination mac and egress port a separate Action data column is added by the compiler. To restrict the table eating up the resources, additional size constraint can be added. Additionally, a default action can be assigned if the table entry does not match.

## Slide 24: P4: Example (V1 model)
Define Control Blocks
  Define Apply
table ipv4_lpm { . . . }
action drop() . . . action ipv4_forward(dstAddr, port) . . .
apply { // Table decider if (hdr.ipv4.isValid()) { ipv4_lpm.apply(); } }
Mem
ALU
}
Notes: Now there can be multiple tables in a single control block. The apply block decides which table to choose. For example, we use ipv4_lpm table if the incoming packet has a valid ipv4 header.

## Slide 25: P4: Example (V1 model)
Define Control Blocks
  Ingress Control Block
control MyIngress(inout headers hdr, inout metadata meta){ action drop() { . . . } action ipv4_forward(macAddr_t dstAddr, egressSpec_t port) { . . . } table ipv4_lpm { . . . } apply { . . . } }
Mem
ALU
Table
Action
}
Apply
Notes: Together, they define the control block.

## Slide 26: P4: Example (V1 model)
Define Rest of the Control Blocks
  Similarly
Parser
De-Parser
MyVerifyChecksum
MyComputeChecksum
MyEgress
MyIngress
Notes: Similarly, rest of the control blocks can be defined. And this slide conclude the example P4 program walkthrough.
Now I understand this is too much information and you do not need to remember unless you are actively working on P4. The reason behind the example was just to show the ease of data plane programming in P4. Additionally, it will help us to understand the objective of the 2 recent papers which will be discussed shortly.

## Slide 27: Benefits of Programmable Data Plane
P4:
Programmability
Easily Add New Feature
Increase Network Reliability
Efficient Use of Resource
Greater Visibility
New Protocols, Apps
Remove unused protocols
Free up resources/ tables
Debug, OAM
(Opn./ Admin./ Mgmt.)
Notes: After the creepy code walkthrough you may have forgot why P4 was introduced. So, let me show who will be benefitted from the P4.
<C> If you want to develop a completely new protocol then you can look into the P4 since P4 is program independent and lets you program your packet handling at data plane level. <C> If you want to debug your networked system, sometime unused protocols can block your visibility. So, using P4 you can remove the unused protocols. This increases visibility as well as network reliability. <C> If someone wants to improve the efficiency of data plane, optimize resource utilization and power consumption, then he/she can take help of P4. <C> Finally, using P4 one can develop telemetric applications and Management tools in data plane.

## Slide 28: P4 Applications: Telemetry
Do we have a good debugging tool?
  Story by Scott Shenker
  YO-YO-MA Philosophy of network debugging
Alternate approach
  Ask a packet:
    Why you are here?
    How did you get here?
    How long did you take?
    What got in your way?
}
None can answer today except P4
https://p4.org/assets/INT-current-spec.pdf
Notes: Here I would like to emphasize on the last benefit i.e. design of telemetric application and why it is required.
Let me tell you a story, which says, there is an IT company. One day there was a service outage and the company was loosing thousands of dollars per minute. So, they assembled a team of engineers to debug the issue. Now the software team came up first and found the bug and fixed it. Then came the database team. They were slow but eventually they found the query which was creating the trouble and they fixed it. The last team was the group of network admins. They were clueless because they only had Ping, Traceroute and SNMP.
This story was told by Scott Shenker. So, I don’t know whether it really had happened or not. I have been to this type of situation multiple time. In fact, both me and Sandip sir were in a similar situation together during a testbed setup in IITG-Wifi-Mesh and I can relate to the clueless part personally. Now according to Scott, network debugging follows only one philosophy. YO-YO-MA. i.e. “Your are Your own mate”.
Network debugging would have been much easier, if I could ask the packets these questions. Why you are here? How did you get here by which path? How long did you take to reach and step-by-step? If you are late, then what got in your way? All these questions can be answered by using P4 based telemetric application.

## Slide 29
Upcoming: P4 Recent Papers
Questions?

## Slide 30: P4:Programming Protocol-independent Packet Processor
Presented By: Subhrendu Chattopadhyay
Systems and Mobile Research Lab, IIT Kharagpur
Notes: Today I’ll be talking about one of recent trends in network architecture i.e. P4 which is formally known as Programming Protocol-independent Packet Processors. But before jumping into the actual topic let me take latitude with the back story.
Recently we were attending Hotnets 2020 and some of the papers were talking about P4 paradigm and data plane. For some of us it was difficult to understand those papers. Therefore, Abhijit asked me whether I can give a short presentation on P4 during our weekly research discussion as I have started exploring this domain.

## Slide 31: Outline
Recap
  Evolution of Programmable network
  Control plane programmability (SDN) & Data plane programmability (PISA)
  P4: Artifacts & Example
  P4: Benefits
P4: Recent Papers
  How to improve network using P4?
P4:
Programmability
Easily Add New Feature
Increase Network Reliability
Efficient Use of Resource
Greater Visibility
Notes: Last week we have seen, why the programmable network came into existence. We have also seen, two types of programmability based on the execution location; (A) SDN Control plane programmability and (B) PISA or Programmable switch architecture for data plane programmability. We have seen, how P4 can provide a high-level programming language and device independent abstraction in PISA match-action pipelines. We have seen the 4 benefits of P4. New feature addition, Improve network reliability, Efficient resource utilization and greater visibility. At the end, we have seen one telemetric application example.
Now as a researcher whenever we learn a new concept or tool we are always thinking, how can we convert it into a paper or how to use it. For that we require literature survey. Today I have hand picked

## Slide 32: P4 Recent Papers:
P4:
Programmability
Easily Add New Feature
Increase Network Reliability
Efficient Use of Resource
Greater Visibility
Debug, OAM
(Opn./ Admin./ Mgmt.)
Notes: Now one of the benefits of P4 was:
By using P4 one can achieve better visibility of the network. One such example is heavy-hitter detection.

## Slide 33: P4 Recent Papers: Heavy-Hitter Detection Entirely in the Data Plane
Heavy-hitter: top k flows by size
Two objectives
  Fast processing
  Accurate result
SDN can not solve it accurately
Data-plane: Hashing for faster processing
  Increases TCAM overhead
Use P4
Sivaraman, Vibhaalakshmi et al. " Heavy-Hitter Detection Entirely in the Data Plane" ACM SOSR 2017
Notes: Heavy-hitters are defined as the flows having more number of packets. Generally, it represents the top k flows in a network eco systems. Now identification of heavy-hitters are easy in a tightly coupled system. But in a distributed settings, it is difficult due to the following reasons. (A) The packet processing can not be affected during the calculation. (B) Once the heavy-hitters are identified some actions are taken. The delay between these detection and action invocation affects the accuracy. SDN with centralized single controller can solve this problem. But scalability is affected. In a distributed control plane the heavy-hitter detection is less accurate. Therefore, people thought that, finding heavy-hitter in data-plane will be more efficient solution. To ensure line rate processing switches require TCAM hardware and hash based state management. TCAMs are costly. So, let’s use P4.

## Slide 34: P4 Recent Papers: Heavy-Hitter Detection Entirely in the Data Plane
Space-saving: Using only k-counters
  Hash-pipe: Exploits pipeline to enable line rate searching
  Table replacement strategy
  Optimization 1: Save state in packet meta-data
  Optimization 2: Find minimum from d out of k entries randomly
  Optimization 2: Split table into d sub-tables
Sivaraman, Vibhaalakshmi et al. " Heavy-Hitter Detection Entirely in the Data Plane" ACM SOSR 2017
Notes: But in P4 also this problem is challenging. Firstly, we need to count the number of packets per flow. If the number of flows are high, then we need a lot of memory to store the number of states, which is counter of packets per flow in this case. Therefore, a space saving solution is inevitable in P4 which employs only k-counters. In this paper the authors have proposed hash-pipe which exploits the match-action pipeline to enable line rate processing. They have stored the counter values in a table with k-rows. But in this case, if a new flow generates significant number of packets, it needs to be added to the table. What happens if the table is already full? Then we need to replace some entries. Now as soon as we replace the flow in the table, the flow counters are lost. On the other hand, in absence of TCAM, we need to reduce the number of table access during the searching of the replacement candidate. So, they have implemented 3 optimization.
1: Save the state inside packet meta data.
2: reduces number of memory access by randomly choosing only d entries out of total k entries of the table.
3: Split the table into d sub-tables for searching which enables parallel access.

## Slide 35: P4 Recent Papers:
P4:
Programmability
Easily Add New Feature
Increase Network Reliability
Efficient Use of Resource
Greater Visibility
Debug, OAM
(Opn./ Admin./ Mgmt.)
Notes: The first paper was about the monitoring and network debugging by using P4 program. But what happens if the P4 program is buggy itself.

## Slide 36: P4 Recent Papers: bf4: towards bug-free P4 programs
P4 is safer than C/C++; Still there are bugs
P4 program behavior depends on table entries inserted by controllers
NAT example: No IPv4  Overwrite Existing data fields
Challenges: Bug-free P4
  Invalid header access
  Array index out-of-bound
  Egress spec not set after ingress
Existing p4v, assert-p4 requires code annotations at compile time
Dumitrescu, Dragos, et al. "bf4: towards bug-free P4 programs." ACM SIGCOMM 2020
Notes: Now debugging the P4 programs are a bit tricky. The program behavior depends on the controllers as well where the controllers are responsible for inserting table entries into the match-action tables. Now during the compile time/ run time there may be some entries which were not handled by the programmer because he/she was unaware of the upcoming controller behavior. For example, a valid P4 program to implement NAT checks the IPv4 header of the packet. Now if there is a valid IPv4 header, it changes the source or destination address. Now if a packet comes with no valid IPv4 header and that is not handled by the P4 programmer it will overwrite some valid header or data field. This is called invalid header access. Similarly, the program may through some array index out of bound due to the absence of a valid header field. Additionally, the programmer may have forgotten to set proper egress specification after the ingress processing.
Now in this paper BF4, the authors have identified these challenges which generates buggy P4 program. They have also said that, the existing tools for P4 debugging requires code annotations which no developer likes.

## Slide 37: P4 Recent Papers: bf4: towards bug-free P4 programs
Contributions
Add extra table keys to rule out invalid table configurations
  60% of them are detected
Use SAT solvers to find invalid table entries which generate bugs
  Takes long  Heuristic
Add P4 controller- P4 Switch intercept module
  Stops invalid table entries found
Dumitrescu, Dragos, et al. "bf4: towards bug-free P4 programs." ACM SIGCOMM 2020
Notes: In this paper the authors have tried to achieve code debugging with out using code annotations. BF4 is a source to source compiler, which takes a buggy P4 program and generates a bug-free P4 program.
The compiler adds some extra table keys to rule out invalid table configurations automatically. Like in the NAT example a table matching should have been added to check valid IPv4 header. They have experimentally shown that, adding these extra checking can reduce the code error in 60% cases. The proposed compiler also uses SAT solvers to rule out the invalid entries. However, the SAT solvers are time consuming. So they have implemented a heuristic version of that. Once those invalid table entries are found, it adds a interceptor module which stops those rules to be installed in the switches even though the controllers instructs them to do so.

## Slide 38: P4 Recent Papers:
P4:
Programmability
Easily Add New Feature
Increase Network Reliability
Efficient Use of Resource
Greater Visibility
New Protocols, Apps
Notes: Apart from monitoring and bug-free programming, P4 promises ease in addition of new features.

## Slide 39: P4 Recent Papers: Do Switches Dream of Machine Learning?: Toward In-Network Classification
Similarity between switch pipeline and ML decision tree
Switch as classification machine
ML to Match-Action mapping
  Observation table
  IISY: In-network Inference made easy
Xiong, Zhaoqi et al. " Do Switches Dream of Machine Learning?: Toward In-Network Classification" ACM HOTNETS 2019
Notes: This next paper tries to implement ML engine inside the data-plane. They have shown that, there is similarity between ML based methods and the match-action pipeline. So, the switches can be considered as a classification machine where the features are the packet headers and the output class is the set of action to be performed on the packet. Now, even though there are similarities, conversion of ML techniques to match-action mapping have many challenges. So they have tested some of the ML designs and identified the suitable ML encoding of popular ML methods that can be converted into the match-action mapping easily. Based on the observations they have proposed a ML environment IISY which can help the developers to implement ML over P4.

## Slide 40: P4 Recent Papers: Do Switches Dream of Machine Learning?: Toward In-Network Classification
Xiong, Zhaoqi et al. " Do Switches Dream of Machine Learning?: Toward In-Network Classification" ACM HOTNETS 2019
Classifier | Per table | Key | Action | Last stage | Suitable?
Decision tree | Feature | Fet. Value | Fet. Code | Table, Decoding code words | Yes
SVM(1) | Class (Hyper plane) | All Fet. | Vote | Logic/table, Votes counting | 
SVM (2) | Feature | Fet. Value | Calculated vector | Logic, hyperplanes calculation | Yes
Naïve bayes (1) | Class & feature | Fet. Value | Probability | Logic, highest probability | 
Naïve bayes (2) | Class | All Fet. | Probability | Logic, highest probability | 
K-means (1) | Class & feature | Fet. Value | Square Distance | Logic, overall distance | 
K-means (2) | Cluster | All Fet. | Distance from Core | Logic, distance comparison | 
K-means (3) | Feature | Fet. Value | Distance vectors | Logic, overall distance | Yes
Notes: Now, the pending question here is what were the observations. And the answer is summarized in this table. For example, they found decision tree as the most suitable candidate.
On the other hand, SVM can be converted to match-action paradigm in two ways.
SVM (1): where all features are inserted into a table. Actions are defined as which side of one hyperplane the data should be placed. Since there are multiple hyperplanes, each decides about data position with respect to one hyperplane. In the final stage all the stage wise decisions are aggregated.
The other way of encoding SVM to match-action is
SVM (2): dedicate one table per feature. Each computes partial support vector. At the end, the total support vector is obtained.
Now, if we look at these two approach, the second one requires smaller table size due to no repetition. Therefore, this encoding produces scalable encoding.
Similarly, they have tested the encoding schemes for Naïve Bayes and K-means and found suitable encoding scheme.

## Slide 41: P4 Recent Papers:
P4:
Programmability
Easily Add New Feature
Increase Network Reliability
Efficient Use of Resource
Greater Visibility
Debug, OAM
(Opn./ Admin./ Mgmt.)
Remove unused protocols
Notes: Apart from new feature addition, P4 can be used for effective resource utilization. This next paper is about two aspects. Network management and Remove unused protocols

## Slide 42: P4 Recent Papers: P5: Policy-driven optimization of P4 pipeline
P4 switches have multiple features like tunneling, NAT, MPLS etc.
Challenges
  Not all traffic require all features
  Not all devices require all features
  Concurrent table lookup based on dependency
Contributions
  Selective deployment of features
  Dependency identification of tables
  Pipeline efficiency improvement
Abhashkumar, Anubhavnidhi, et al. "P5: Policy-driven optimization of p4 pipeline." ACM SOSR 2017
Notes: So far we have seen that, P4 can open up new horizon of data plane programmability. Therefore, multiple paper have tried to implement NFV using P4. Now, a P4 switch can have multiple features. For example, in P4 source repo there is a switch.p4 sample. This is a consolidated switch code which is complicated and contains around 130 tables like tunneling, NAT, MPLS etc. Now, if we deploy switch.p4 directly, it is going to waste too much resource. Because, not all flows require all functionalities. So, all device does not require all functionalities. Additionally, there is a scope of parallel processing by placing multiple table to a single stage provided there is no dependency among them.
Therefore, in this paper the authors have designed P5 system which can enable selective deployment of features. It can also identify the table dependencies and based on the tables, it can improve the pipeline efficiency by stage wise table optimization.

## Slide 43: P4 Recent Papers:
P4:
Programmability
Easily Add New Feature
Increase Network Reliability
Efficient Use of Resource
Greater Visibility
Free up resources/ tables
Debug, OAM
(Opn./ Admin./ Mgmt.)
Notes: In the previous paper we have seen how P4 can be used for management and resource optimization. This next paper is also in the similar direction.

## Slide 44: P4 Recent Papers: Composing Dataplane Programs with µP4
P4 is monolithic
Heterogenous Programming Model
  State machine based parser and Match-Action based control
  L2 and L3 forwarding example
    L2.parser  L2.ingress  L2.egress  L3 parser  L3.ingress  L3.egress
Tightly coupled to switch architecture
Soni, Hardik, et al. "Composing Dataplane Programs with μP4.” ACM SIGCOMM 2020
Notes: Similar to the earlier paper this paper too tackles the monolithic code structure of P4 programs. Additionally, this paper tries to reduce the heterogeneity of the P4 programming model.
As we have seen in our last presentation, the control block for parser implements a state machine which is different than match-action pipeline. Essentially composition of parser block with any other control block is difficult. For example, if I have two modules; one for L2 forwarding and one for L3 forwarding, each having a different parser then there is no-way I can compose these two parsers together. In such case there will be two different parser.
Another problem in P4 is the program written specific to one switch architecture may not be used for another architecture without significant rewriting of code. For example, let’s consider two different switch model. V1 model mentioned previously and Flex model. Now in Flex model each stage needs to be arranged in accordance to TCP/IP layers. Therefore, one P4 code written for V1 model can run in Flex model.

## Slide 45: P4 Recent Papers: Composing Dataplane Programs with µP4
Contribution:
Source–to-source compiler
  Multiple µP4 program  Fullscale P4 program
Higher level abstraction for heterogeneous target architecture
  Use logical pipeline [Parser  Control  Deparser]
Soni, Hardik, et al. "Composing Dataplane Programs with μP4.” ACM SIGCOMM 2020
Notes: In this paper, the authors have developed a intermediate compiler which handles heterogeneity and model specific code writing. They provide a separate library which takes multiple µP4 programs and generates one full scale P4 program. Now using this tool, multiple µparser can be composed together to generate a full parser. Depending on the target architecture, the compiler can rearrange the µcontrol blocks so that the developer don’t have to write architecture specific program.

## Slide 46: P4 Recent Papers: Summary
Paper | Conf | Paper Idea | P4 Benefit
Heavy-hitter | SOSR’17 | Detect heavy-hitter flows | Network debugging
BF4 | SIGCOMM’20 | Generate bug free P4 program | Network debugging
IISY | HOTNETS’19 | Use P4 switches for ML encoding | Feature addition
P5 | SOSR’17 | P4 table arrangement | Remove unused protocols & network management
µP4 | SIGCOMM’20 | Break P4 into small parts | Resource optimization & network management
P4 Wrapper compiler
Notes: With this paper let me summarize the 5 papers we have seen today. In the first two papers, we have seen improved network debugging by using P4. The third paper IISY, tried to add new feature like embedding ML frameworks inside data plane switches. Next we have seen P5 where unused protocols can be removed to achieve better network management. The last one, µP4 was about optimization of resources and NFV management. One more observation, the recent works 3 out of these 5 papers proposed a wrapper compiler and language level optimization.

## Slide 47
Questions?
Any new idea?
Thank You

## Slide 48: P4 Recent Papers: Enabling a Permanent Revolution in Internet Architecture
Internet thin waist architecture
  is inherently ﬂawed
  is deeply entrenched
Future internet architectures did not succeed
  Backward compatibility
  Incrementally deployable
Solution Approach:
  Inter-domain delivery should be an overlay on intra-domain delivery
  Introduce L3.5  Trotsky Processor
  Deployment should start at edge
McCauley, James, et al. "Enabling a permanent revolution in internet architecture." ACM SIGCOMM 2019
Notes: This paper does not use P4. But utilizing P4 for the proposed problem would have great. I have presented this paper earlier. So let me go through it briefly once more.

## Slide 49: P4 Recent Papers: Enabling a Permanent Revolution in Internet Architecture
Implementation challenge
Deployment challenge
Can be implemented using P4
McCauley, James, et al. "Enabling a permanent revolution in internet architecture." ACM SIGCOMM 2019

## Slide 50: P4 Recent Papers:
P4:
Programmability
Easily Add New Feature
Increase Network Reliability
Efficient Use of Resource
Greater Visibility
New Protocols, Apps
Notes: Add new feature ML engine in data plane.

## Slide 51: P4 Recent Papers:
P4:
Programmability
Easily Add New Feature
Increase Network Reliability
Efficient Use of Resource
Greater Visibility
New Protocols, Apps
Remove unused protocols
Free up resources/ tables
Debug, OAM
(Opn./ Admin./ Mgmt.)

## Slide 52: P4 Recent Papers: P4NFV: An NFV Architecture with Flexible Data Plane Reconfiguration
Mohammadkhan, Ali, et al. "P4NFV: P4 Enabled NFV Systems with SmartNICs," IEEE CNSM 2018, IEEE NFV-SDN 2019,